## Slide 1
<_>
<rects>
<_>
0 6 60 7 -1.</_>
<_>
15 6 30 7 2.</_>
</rects>
<tilted>0</tilted></_>
<_>
60x60 square
(x,y)=(0,6)
60 wide
7 tall
-Everything referenced to a 60x60 square
-Coordinates of top left corner are (0,6)
-width = 60 and height = 7
-multiply the sum of the pixels in this rectangle by -1

## Slide 2
<_>
<rects>
<_>
0 6 60 7 -1.</_>
<_>
15 6 30 7 2.</_>
</rects>
<tilted>0</tilted></_>
<_>
60x60 square
(x,y)=(15,6)
30 wide
7 tall
-Coordinates of top left corner are (15,6)
-width = 30 and height = 7
-multiply the sum of the pixels in this rectangle by +2

## Slide 3
60x60 square
-This is the first Haar-like feature in the rectangle list at the end of the .xml file
-Effectively, the code takes the difference between the “sum of the pixels in the black area” and the “sum of the pixels in the white area”.
-Let P(large) be the sum of the pixels in the large 60x7 rectangle.
-Let P(small) be the sum of the pixels in the small 30x7 rectangle.
-The code multiplies P(large) by -1 and P(small) by +2 and adds them together. This gives: -P(large) + 2P(small)
-The net effect is that you get +1 times the pixel sum in the black region and -1 times the pixel sum of the white region in the picture at left. This is compared to a threshold to see if it meets the criteria.